## Slide 1: ENVIAR WHATSAP

## Slide 2: OBJETIVOS
COMO ENVIAR EMAIL POR RASPBERRY PI
COMO ENVIAR EMAIL POR ESP32
COMO ENVIAR EMAIL POR ESP8266

## Slide 3: TWILIO
www.twilio.com.
Crear cuenta en www.twilio.com
Verifique su numero
Navegar a SMS chatbot
Darle nombre al proyecto
Ir a Programar SMS
Ir a WhatsApp
Activar sandbox
Provea un numero de WhatsApp y un codigo
Copie la cuenta SID y el token

## Slide 4: PYTHON
Instale libreria twilio
pip install twilio
Descargue libraría help
https://www.twilio.com/docs/python/install
from twilio.rest import Client

## Slide 5: PYTHON
account_sid = 'AC1d8ea8f74323a'
auth_token = 'your_token'
client = Client(account_sid, auth_token)
message = client.messages.create(
body='Hello there!',
from_='whatsapp:+14155238886',
to='whatsapp:+15005550006')
print(message.sid)

## Slide 6: ESP8266 – ESP32
#include <ESP8266WiFi.h>
#include <WiFiClient.h>
#include <ESP8266WebServer.h>
#include <ESP8266HTTPClient.h>
const char *ssid = "";
const char *password = "";

## Slide 7: ESP8266 – ESP32
void setup() {
delay(1000);
WiFi.mode(WIFI_OFF);
delay(1000);
WiFi.mode(WIFI_STA);
WiFi.begin(ssid, password);
while (WiFi.status() != WL_CONNECTED) {
delay(500);
}
}

## Slide 8: ESP8266 – ESP32
id= "Twilio_SID";
token = "Twilio_Token";
from = "14151234567";
to = "14081234567";
// %0A = \n
message = "mensaje %0A otra linea";
// Your hedron from TheAmplituhedron
HEDRON = "TheAmplituhedron_Hedron";

## Slide 9: WEBHOOK PATH
WebHook = "https://www.theamplituhedron.com/dashboard/WhatsApp-Web-Hook/" + HEDRON + ".php?id=" + id + "&token=" + token + "&body=" + message + "&from=" + from + "&to=" + to;

## Slide 10: ESP8266 – ESP32
HTTPClient http;
http.begin(WebHook, fingerprint);
int httpCode = http.GET();
String payload = http.getString();
if(httpCode == 200){ Serial.println("\n Successfully..."); }else{ Serial.println("\n Error Code: " + httpCode); }
http.end();

## Slide 11: Gracias por su atención.